MATERIAL SAFETY DATA SHEET

| IDENTIFICATION Company Name & Address Hi-Chem NZ Ltd t/a Cyndan Chemicals P O Box 72-088, Papakura Auckland, New Zealand Telephone: (09) 298 5635 Fax: (09) 298 5422 Email: hi-chem@ihug.co.nz |
| --- |
| Product Name: | Green Reaper | U.N. No.: | Nil |
| Trade Name: |  | Class: | Nil |
| Other Names: |  | Subsidiary Class: |  |
| Manufacturers Code: |  | Hazchem Code: | Nil |
|  |  | Toxic Substance: | Nil |
| Use: | Weed Killer |
| PHYSICAL DESCRIPTION/PROPERTIES |
| Appearance: | Clear, thin liquid. Distinctive odour |
| Boiling Point (°C): | 250 |
| Vapour Pressure (mm Hg@25°C) | <1 |
| Per Cent Volatiles: | 0 |
| Specific Gravity @ 20°C: | 0.95 |
| Flash Point (°C): | 135 |
| Flammability Limits (%): | Not established |
| Auto ignition Temperature (°C) | Not Established |
| Plus other properties if applicable | Will emulsify with water |
| INGREDIENTS |
| Chemical Entity | Proportion |
| (include all hazardous ingredients) | (low<10%>medium<60%>high) |
| C8 – C10 Fractions of Coconut Fatty Acids | High |
| Sugar/fatty Acid esters | Medium |
| HEALTH HAZARD INFORMATION |
| HEALTH EFFECTS |
| Swallowed: | May cause irritation |
| Eyes: | Transient irritation |
| Skin: | No adverse effect expected |
| Inhaled: | Inhalation of spray mist may irritate throat |
| FIRST AID |
| Swallowed: | Rinse mouth. Drink plenty of water. Do not induce vomiting. Obtain advice from doctor if concerned. |
| Eyes: | Rinse thoroughly with water |
| Skin: Inhaled | Remove contaminated clothing. Flush area with water. Launder clothing before reuse. Move to fresh air. |

| PRECAUTIONS FOR USE |
| --- |
| Advice to Doctor: | If material is ingested, it may be aspirated into the lungs and cause chemical pneumonitis. Treat appropriately. |
| Exposure Limits: | Ingestion : LD50 (Rat) >20000mg/kg Dermal: LD50 (Rabbit) >2000mg/kg Aquatic: LC50 Fish between 100 and 500 mg/L depending on species EC50 Crustaceans 235mg/L |
| Ventilation: | Not required |
| Personal Protection: | No special precautions required |
| Flammability | Low flammability. Will support combustion under extreme conditions of a fire. Cool containers with water spray to prevent rupture. Extinguish using Carbon Dioxide, dry chemical foam or water fog. |
| SAFE HANDLING INFORMATION |
| Storage and Transport | Store in original and labelled containers in dry conditions. Do not transfer to metal containers. Do not store with Oxidisers |
| Spills and Disposal | Absorb spill with sand, earth etc and transfer to plastic wheely bin for disposal. |
| Fire and Explosion | Combustion by-products are Carbon Dioxide, Carbon Monoxide and water |
| Hazard |  |
| Other Information | Biodegradability: OECD 301D method: 81-86% BOD28/COD |